## Slide 1
COMPUTER ARCHITECTURE & ORGANIZATION
ADDRESSING MODES
& INSTRUCTION FORMATS
How a CPU finds data and decodes each instruction
William Stallings • Chapter 13 topic set
Definitions • Diagrams • Advantages & limitations • x86/ARM examples • Activities
CPU
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
01

## Slide 2
Learning outcomes
START HERE
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
02
Define addressing modes and explain why CPUs need them
Calculate effective addresses for common modes
Compare x86 and ARM addressing patterns
Read instruction formats and identify their fields
Interpret simple assembly language and trace execution
By the end
You should be able to explain where an operand comes from, how an instruction is encoded, and why different designs make different trade-offs.
Learning routine
Predict → Discuss → Trace → Explain

## Slide 3
Warm-up: where is the value 25?
ENGAGE
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
03
MOV R0, #25
LDR W0, [X1, #8]
Question 1
In the first instruction, where is 25 stored?
Question 2
In the second instruction, what does X1 + 8 represent?
Think for 30 seconds, discuss with a partner, then share your reasoning.
Note: examples use simplified assembly syntax; exact syntax varies by ISA and assembler.

## Slide 4
4.1 Addressing modes: definition and purpose
FOUNDATION
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
04
Definition
An addressing mode is the rule an instruction uses to identify an operand or calculate where that operand is located.
Why do we use them?
Programs work with constants, registers, arrays, pointers, stack values, and memory objects. One way to locate data cannot serve every need efficiently.
Instruction
LOAD R0, [R1,#4]
Address rule
R1 + 4
Memory
Read value
The mode tells the CPU how to interpret the operand field: as a value, a register, or a route to a memory address.

## Slide 5
Effective address: the key idea
FOUNDATION
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
05
Definition
Effective address (EA) = the memory address calculated from the instruction's addressing rule.
EA = base register + offset
Example: X1 = 1000, offset = 8
X1
1000
Offset
#8
EA
1008
If the instruction is LDR W0, [X1, #8], the CPU reads data from memory address 1008; it does not load the number 8.
Quick check: if X1 = 2040 and offset = 12, what is EA?

## Slide 6
4.1 Immediate addressing
ADDRESSING MODES
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
06
Definition
The operand value is encoded inside the instruction.
MOV R0, #25
Best used for
Constants, counters, masks, small offsets.
Advantages
Fast access; no separate data-memory read for the constant; code can be concise.
Limitations
Immediate values may have size or encoding restrictions; large constants may need multiple instructions or literal loads.
Ask: in MOV R0, #25, is 25 a memory address or the actual value?

## Slide 7
4.1 Register addressing
ADDRESSING MODES
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
07
Definition
The operand is held in a CPU register named by the instruction.
ADD R0, R1
Register bank (concept)
R0 7
R1 5
R2 —
Advantages
Very fast; avoids a data-memory access; useful for repeated calculations.
Limitations
Register count is limited. Values may need loading into registers first; register allocation is important.
Practice: if R0 = 7 and R1 = 5, what value does ADD R0, R1 produce in a two-operand style?

## Slide 8
4.1 Direct (absolute) addressing
ADDRESSING MODES
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
08
Definition
The instruction specifies a memory address directly, or encodes an address/displacement that identifies a location.
LOAD R0, [1000]
Example
If memory[1000] = 42, the loaded value is 42.
Memory (simplified)
Addr 1000
Value: 42
Addr 1004
Value: 17
Addr 1008
Value: 99
Advantages / limits
Simple and explicit. But fixed addresses can make code less relocatable and may require more bits to encode.
Conceptual example only: many modern instructions use base-plus-displacement rather than a full absolute address.

## Slide 9
4.1 Register-indirect addressing
ADDRESSING MODES
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
09
Definition
A register contains the memory address of the operand.
LOAD R0, [R2]
R2
1000
Mem[1000]
42
Advantages
Excellent for pointers, linked lists, dynamic data, and arrays; the address can change without rewriting the instruction.
Limitations
May require a load to obtain the pointer first; dependent memory accesses can add latency.
Explain: why is it useful for a linked list if each node points to the next node?

## Slide 10
4.1 Base + displacement / indexed addressing
ADDRESSING MODES
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
10
Definition
The effective address is formed from a base register plus a constant offset; indexed forms may add an index or scaled index.
LDR W0, [X1, #8]
MOV EAX, [RDI+8]
Why use it?
Arrays, structures, stack frames, and fields in objects.
Array of 4-byte integers
A[0]
@ 1000
A[1]
@ 1004
A[2]
@ 1008
A[3]
@ 1012
Address of A[i] = base + i × element_size
For A[2]: 1000 + 2 × 4 = 1008
Advantage: compact and flexible. Limitation: offset range and scaling rules depend on the ISA and instruction.

## Slide 11
4.1 Stack and PC-relative addressing
ADDRESSING MODES
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
11
Stack-based addressing
The stack pointer (SP) identifies the top of a stack. PUSH/POP or load/store patterns access values relative to the stack.
PC-relative addressing
The address is calculated from the program counter plus an offset. Common for branches and position-independent code.
Stack grows (conceptually)
Top / SP
Saved R1
Return addr
PC
0x1000
Offset
+0x20
Target
0x1020
Useful for function calls, local variables, branches, and relocatable code.

## Slide 12
4.1 Addressing modes: choose the right tool
RECAP
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
12
Mode
Operand location
Main advantage
Main limitation
Immediate
Inside instruction
Fast constants
Value range may be limited
Register
CPU register
Very fast
Few registers
Direct / absolute
Address specified
Simple to understand
Relocation / encoding cost
Register indirect
Address held in register
Flexible pointers
Pointer dependency
Base + offset
Base register + displacement
Excellent for arrays/fields
Offset/scaling limits
PC-relative
PC + displacement
Relocatable branches/data
Reach may be limited
Pair challenge: choose an addressing mode for (1) constant 10, (2) array element A[3], (3) pointer to a node.

## Slide 13
4.2 x86 and ARM addressing modes
ISA COMPARISON
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
13
x86-64 patterns
• Immediate: MOV EAX, 5
• Register: ADD EAX, EBX
• Base + displacement: MOV EAX, [RDI+8]
• Indexed: MOV EAX, [RDI+RCX*4+8]
• Stack operations: PUSH, POP
x86 offers rich memory operand forms, but legal forms vary by instruction.
ARM AArch64 patterns
• Immediate: MOV W0, #5
• Register: ADD W0, W1, W2
• Base + offset: LDR W0, [X1, #8]
• Register offset: LDR W0, [X1, X2]
• Stack: SP-based load/store patterns
ARM arithmetic generally uses registers; memory is accessed explicitly with load/store instructions.
Remember: both ISAs support several ways to access operands, but their syntax, restrictions, and encoding details differ.

## Slide 14
4.2 x86-64: base + index × scale + displacement
ISA COMPARISON
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
14
MOV EAX, [RDI + RCX*4 + 8]
Effective address
RDI + (RCX × 4) + 8
Base
RDI = 1000
+
Index
RCX = 2
+
Scale
4
+
Disp.
8
Calculation
1000 + (2 × 4) + 8 = 1016
Why useful?
Compact access to array elements and fields.
Note: x86 scale factors are commonly 1, 2, 4, or 8; the exact form must be supported by the addressing encoding.

## Slide 15
4.2 ARM AArch64: load/store addressing
ISA COMPARISON
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
15
LDR W0, [X1, #12]
Meaning
Read 32 bits from address X1 + 12 into W0.
Four-byte array elements
A[0]
addr 1000
A[1]
addr 1004
A[2]
addr 1008
A[3]
addr 1012
Why offset 12?
If X1 is the array base and each element is 4 bytes, offset 12 reaches element A[3].
Advantages / limitation
Regular load/store model is easier to reason about. Offset ranges and alignment rules depend on instruction form.
Student prompt: what offset reaches A[2] when each element is 4 bytes?

## Slide 16
4.3 Instruction formats: definition and fields
INSTRUCTION FORMATS
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
16
Definition
An instruction format is the arrangement of bits that encodes the operation, registers, addressing information, and sometimes an immediate value.
OPCODE
REG
REG
MODE / IMM
Why use formats?
The CPU must decode bit patterns reliably. Consistent fields help hardware identify the operation and operands.
Trade-offs
More fields can express more choices but consume bits. Regular formats simplify decoding; compact formats can improve code density.
This is a conceptual diagram—not a universal encoding. Each ISA defines its own exact bit positions.

## Slide 17
4.3 Instruction format design: advantages and disadvantages
INSTRUCTION FORMATS
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
17
Fixed-length formats
Advantages:
• Easier instruction boundaries
• Predictable fetch/decode
Limitations:
• Some instructions may use bits inefficiently
Variable-length formats
Advantages:
• Can encode simple instructions compactly
• Good code density
Limitations:
• More complex instruction-boundary decoding
Hybrid / compressed
Some architectures support multiple instruction lengths or compact subsets to balance code size and decode complexity.
Fixed-size example
B1
B2
B3
B4
Variable-size example
1B
2B
1B
3B
Ask: which design is easier to decode? Which can save space?

## Slide 18
4.3 Common instruction fields
INSTRUCTION FORMATS
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
18
Opcode
Which action? ADD, LOAD, BRANCH
Register field(s)
Which register(s) supply or receive values?
Addressing / mode bits
How should operand fields be interpreted?
Immediate / displacement
Constant or offset encoded in the instruction
Condition / modifier
Optional condition, width, shift, or variant information
Not every instruction has every field. The encoding depends on the ISA and the operation.

## Slide 19
4.4 x86-64 instruction format
ISA COMPARISON
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
19
Key fact
x86 instructions are variable length (up to 15 bytes in 64-bit mode).
Prefixes
Opcode
ModR/M
SIB
Disp.
Imm.
Why so many fields?
x86 supports many operand combinations, legacy compatibility, prefixes, and flexible memory addressing.
Benefits and cost
Benefit: compact encodings and rich forms. Cost: decoding is more complex and instruction length is less predictable.
Not all fields are present in every instruction; this diagram shows possible components, not a fixed layout.

## Slide 20
4.4 ARM AArch64 instruction formats
ISA COMPARISON
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
20
Key fact
AArch64 base instructions are 32 bits wide, with different encoding classes for different instruction families.
Illustrative 32-bit instruction word
OP / class
Registers
Immediate / mode
Benefits
Regular width simplifies instruction-boundary identification and supports predictable decode.
Trade-offs
Different instruction classes still have different field layouts; constants or addresses may need multiple instructions.
ARM also has other architecture states and instruction sets historically; this slide focuses on AArch64.

## Slide 21
4.5 Assembly language: definition and role
ASSEMBLY
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
21
Definition
Assembly language is a human-readable representation of machine instructions using mnemonics, registers, labels, and operands.
Why use it?
To inspect low-level behavior, debug performance-sensitive code, understand compiler output, and interact with hardware or system interfaces.
MOV W0, #7
ADD W0, W0, #5
; W0 = 12
Assembly vs machine code
Assembly uses readable mnemonics. The assembler translates them into encoded instruction bytes/bits.
Assembly is still architecture-specific: x86 assembly will not normally run unchanged on ARM.

## Slide 22
4.5 From assembly to execution
ASSEMBLY
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
22
Source
program.s
Assembler
mnemonics → bits
Object file
machine code + symbols
Linker
combine code/libraries
CPU
fetch, decode, execute
Assembler: translates mnemonics. Linker: resolves symbols and combines modules. Loader: places the executable in memory.
Advantage
Precise control and excellent visibility into registers and memory.
Limitation
More architecture-specific, harder to maintain, and often less portable than high-level code.

## Slide 23
4.5 Read an assembly instruction
ASSEMBLY
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
23
LDR W0, [X1, #8]
LDR
Mnemonic / operation
W0
Destination register
[X1, #8]
Memory operand
X1 + 8
Effective address rule
Assume X1 = 1000 and memory[1008] = 77.
Predict
After the instruction, what value is in W0?
Answer
W0 = 77; the offset selects address 1008.

## Slide 24
Worked example: access A[3]
WORKED EXAMPLE
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
24
Given
Base address = 2000
Each integer = 4 bytes
EA = base + i × size
Index
i = 3
Calculation
2000 + 3 × 4 = 2012
A[0]
2000
A[1]
2004
A[2]
2008
A[3]
2012
A[4]
2016
Question: if each element were 8 bytes instead, what would be the address of A[3]?

## Slide 25
Design trade-offs: why no single mode wins
DISCUSSION
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
25
Speed
Registers are usually fast. Memory-based operands may need additional memory access and can be affected by cache behavior.
Code size
Immediate values and compact encodings can save instructions; large constants or complex addressing may require extra bytes/instructions.
Flexibility
Indirect and indexed modes support pointers and arrays, but require more complex address calculations or encoding rules.
Small-group question: if you were designing an ISA for a battery-powered device, what trade-off would matter most and why?
Remember
The best design balances hardware complexity, performance, code density, compiler needs, and backward compatibility.

## Slide 26
Pair activity: decode, calculate, explain
INTERACTIVE
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
26
Task A
R1 = 500; decode LOAD R0, [R1, #12]. Calculate EA.
Task B
RDI = 1000, RCX = 3. Calculate [RDI + RCX*4 + 8].
Task C
Explain one benefit and one limitation of variable-length instructions.
Instructions: 3 minutes in pairs, then one pair presents its calculation and another pair checks it.
A: EA = 500 + 12 = 512
B: EA = 1000 + (3 × 4) + 8 = 1020
Instructor: ask students to explain the formula, not just state the answer.

## Slide 27
Knowledge check: no notes for 60 seconds
QUIZ
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
27
1
1. What is an addressing mode?
Answer: Rule for locating or interpreting an operand
2
2. What does #5 usually indicate in these examples?
Answer: Immediate constant 5
3
3. What is EA for base 300 + offset 16?
Answer: 316
4
4. Which ISA has variable-length instructions: x86-64 or AArch64?
Answer: x86-64
5
5. What does an assembler do?
Answer: Translates assembly mnemonics to machine code
Instructor: cover the answer column for the first round, then use peer marking.

## Slide 28
Exit ticket: connect the concepts
WRAP-UP
COMPUTER ARCHITECTURE • ADDRESSING MODES & FORMATS
28
Explain
What is the difference between an operand value and an effective address?
Apply
Write an instruction that loads a value from base register X1 plus offset 16.
Evaluate
Give one advantage and one limitation of x86 variable-length formats.
Take-home task: show how to access A[4] in an array of 4-byte integers using a base address and an index.
Reading
William Stallings, Computer Organization and Architecture: addressing modes, instruction formats, and assembly language. Page numbers vary by edition.
Slides use teaching examples and original diagrams; verify exact syntax against the architecture/assembler used in your lab.